Wolmer’s Trust High School for Girls

CAPE COMPUTER SCIENCE

Upper and Lower Six					Teacher:  Mrs.   McCallum-Rodney

Access Methods for mobile network

Code Division Multiple Access (CDMA)

CDMA strives to better utilize the radio spectrum by allowing multiple users to share the same physical channel.  More than one person can carry on a conversation on the same frequency without causing interference.

CDMA let everyone transmit at the same time. Conventional wisdom would lead you to believe that this is simply not possible. Using conventional modulation techniques, it most certainly is impossible. What makes CDMA work is a special type of digital modulation called "Spread Spectrum". This form of modulation takes the user's stream of bits and splatters them across a very wide channel in a pseudo-random fashion. The "pseudo" part is very important here, since the receiver must be able to undo the randomization in order to collect the bits together in a coherent order.

Imagine a room full of people, all trying to carry on one-on-one conversations.  In CDMA each couple talks at the same time, but they all use a different language. Because none of the listeners understand any language other than that of the individual to whom they are listening, the background din doesn't cause any real problem.

For radio systems there are two resources, frequency and time. Division by frequency, so that each pair of communicators is allocated part of the spectrum for all of the time, results in Frequency Division Multiple Access (FDMA). Division by time, so that each pair of communicators is allocated all (or at least a large part) of the spectrum for part of the time results in Time Division Multiple Access (TDMA). In Code Division Multiple Access (CDMA), every communicator will be allocated the entire spectrum all of the time. CDMA uses codes to identify connections.

Multiple Access Schemes

CDMA uses unique spreading codes to spread the baseband data before transmission. The signal is transmitted in a channel, which is below noise level. The receiver then uses a correlator to despread the wanted signal, which is passed through a narrow bandpass filter. Unwanted signals will not be despread and will not pass through the filter. Codes take the form of a carefully designed one/zero sequence produced at a much higher rate than that of the baseband data. The rate of a spreading code is referred to as chip rate rather than bit rate. 
See coding process page for more details.

CDMA spreading

CDMA codes are not required to provide call security, but create a uniqueness to enable call identification. Codes should not correlate to other codes or time shifted version of itself. Spreading codes are noise like pseudo-random codes, channel codes are designed for maximum separation from each other and cell identification codes are balanced not to correlate to other codes of itself.

Time Division Multiple Access (TDMA)

Division by time, so that each pair of communicators is allocated all (or at least a large part) of the spectrum for part of the time results in Time Division Multiple Access (TDMA).

TDMA strives to better utilize the radio spectrum by allowing multiple users to share the same physical channel.  More than one person can carry on a conversation on the same frequency without causing interference.

TDMA does it by chopping up the channel into sequential time slices. Each user of the channel takes turns transmitting and receiving in a round-robin fashion. In reality, only one person is actually using the channel at any given moment, but he or she only uses it for short bursts. He then gives up the channel momentarily to allow the other users to have their turn. This is very similar to how a computer with just one processor can seem to run multiple applications simultaneously.

Imagine a room full of people, all trying to carry on one-on-one conversations. In TDMA each couple takes turns talking. They keep their turns short by saying only one sentence at a time. As there is never more than one person speaking in the room at any given moment, no one has to worry about being heard over the background noise.

Global System for Mobile Communication (GSM)

GSM (Global System for Mobile communication) is a digital mobile telephone system that is widely used in Europe and other parts of the world.

GSM uses a variation of Time Division Multiple Access (TDMA) and is the most widely used of the three digital wireless telephone technologies (TDMA, GSM, and CDMA). GSM digitizes and compresses data, then sends it down a channel with two other streams of user data, each in its own time slot. It operates at either the 900 MHz or 1,800 MHz frequency band.

GSM is the de facto wireless telephone standard in Europe. GSM has over one billion users worldwide and is available in 190 countries. Since many GSM network operators have roaming agreements with foreign operators, users can often continue to use their mobile phones when they travel to other countries.

General Packet Radio Service (GPRS)

General Packet Radio Services (GPRS) is a packet-based wireless communication service that promises data rates from 56 up to 114 Kbps and continuous connection to the Internet for mobile phone and computer users.

The higher data rates allow users to take part in video conferences and interact with multimedia Web sites and similar applications using mobile handheld devices as well as notebook computers.

GPRS is based on Global System for Mobile (GSM) communication and complements existing services such circuit-switched (Circuit-switched is a type of network in which a physical path is obtained for and dedicated to a single connection between two end-points in the network for the duration of the connection) cellular phone connections and the Short Message Service (SMS).

GPRS (General Packet Radio Service) is a packet based communication service for mobile devices that allows data to be sent and received across a mobile telephone network. GPRS is a step towards 3G and is often referred to as 2.5G. Here are some key benefits of GPRS:

- Speed

GPRS is packet switched. Higher connection speeds are attainable at around 56–118 kbps, a vast improvement on circuit switched networks of 9.6 kbps. By combining standard GSM time slots theoretical speeds of 171.2 kbps are attainable. However in the very short term, speeds of 20-50 kbps are more realistic.

- Always on connectivity

GPRS is an always-on service. There is no need to dial up like you have to on a home PC for instance. This feature is not unique to GPRS but is an important standard that will no doubt be a key feature for migration to 3G. It makes services instantaneously available to a device.

- New and Better applications

Due to its high-speed connection and always-on connectivity GPRS enables full Internet applications and services such as video conferencing straight to your desktop or mobile device. Users are able to explore the Internet or their own corporate networks more efficiently than they could when using GSM. There is often no need to redevelop existing applications.

- GSM operator Costs

GSM network providers do not have to start from scratch to deploy GPRS. GPRS is an upgrade to the existing network that sits along side the GSM network. This makes it easier to deploy, there is little or no downtime of the existing GSM network whilst implementation takes place, most updates are software so they can be administered remotely and it allows GSM providers to add value to their business at relatively small costs.

The GSM network still provides voice and the GPRS network handles data, because of this voice and data can be sent and received at the same time.